VL-100C / VL-100CM

CNC Vertical Lathes

###### with Fanuc Control

January 2013

STANDARD FEATURES

| MANUAL 4-JAW CHUCK (39.3”) | ELECTRIC TORQUE LIMIT |
| --- | --- |
| HEAT EXCHANGER FOR SPINDLE BEARING & GEAR | LEVELING BOLTS & PADS |
| Complete Splash Guard FULL ENCLOSURE | CHIP CONVEYOR, HINGE TYPE |
| HYDRAULIC POWER UNIT | CHIP TROLLEY |
| COOLANT THRU TOOL HOLDER | TOOL HOLDERS |
| AUTOMATIC LUBRICATION SYSTEM | SPINDLE ORIENTATION |
| SPINDLE CHILLER FOR GEARBOX AND SPINDLE | ELECTRICAL & HYDRAULIC CIRCUIT DIAGRAM MANUAL |
| WORK LIGHT | FANUC CONTROL MANUAL |
| STATUS LIGHT (R/Y/G) | OPERATION & MAINTENANCE MANUAL |
| WORKPIECE COUNTER | SERVICE TOOL BOX & TOOL KITS |
| COOLANT SYSTEM WITH TANK | HEAT EXCHANGER FOR ELECTRICAL CABINET |
| COOLANT BED SHOWER SYSTEM |  |

# BASIC MACHINE SPECIFICATIONS

VL-100C FIXED RAIL CAPACITIES

Maximum Swing Diameter				47.26”

Maximum Turning Diameter				47.24”

Maximum Turning Height				25.59”

Vertical Travel (Z-Axis)				23.62”

Cross-section of Ram   			          7.87” x 7.87”

Horizontal Travel (X-Axis)                                   				L -3.93” / R +27.56

Distance from Ram to Table				12.82”- 36.42”

Maximum Work Piece Weight				7,700 lbs.

Cross-Rail Travel				Fixed

VL-100C PROGRAMMABLE RAIL CAPACITIES (Optional)

Maximum Swing Diameter				47.26”

Maximum Turning Diameter				47.24”

Maximum Turning Height				37.4”

Vertical Travel (Z-Axis)				27.56”

Horizontal Travel (X-Axis)				L -3.93” / R +27.56

Distance from Ram to Table				19.7”- 43.31”

Maximum Work Piece Weight				7,700 lbs.

Cross-Rail Travel (Programmable by M-code in Auto)			23.6” (3 X 7.87” Steps)

* Machines fitted with the optional power chuck adapter, please subtract 2.9” from “Maximum Turning Height”

* Honor Seiki’s moveable rail is programmable by M-code, this allows for a continuous turning operation

as the rail is moved and re-positioned in the memory mode.

SPINDLE

Spindle RPM				3-400 RPM

Table Diameter				39.3

2 Speed Heavy Duty Gear box				2-Step	s

Spindle Torque				10,700 ft-lbs.

Spindle Bearing Diameter				18”

Spindle Bearing Manufacturer				Timken/PSL/THK

Height of Spindle Face from Floor				39.3”

ATC SYSTEM – VL100C

Number of Tools				12

Tool Size				32mm / 1.25”

Cross-section of Ram				7.87” x 7.87”(200 x 200mm)

ATC SYSTEM – VL100CM (With Milling Capabilities)

Number of Tools 				12 (16 Optional)

Live Tool Spindle Speed (VL-100CM)				50-2250

Spindle HP			           20 HP

Tool Size				32mm / 1.25”

Cross-section of Ram				8.66” x 8.66” (220 x 220mm)

C-Axis				0.001”

*Standard Supplied Tool holders for the C and CM are listed under Tooling Options

FEEDS

Rapid Traverse Rate X, Z				393 IPM

Horizontal Travel (X-Axis)				-3.93” / +27.56

Vertical Travel (Z-Axis)				23.62”

X-Axis Axial Thrust				2,684 lbs.

Z-Axis Axial Thrust				2,684 lbs.

Positioning Accuracy				± .0003” (Full Stroke)

Repeatability				± .0002”

MOTORS

Spindle Motor Power				AC 50HP (60HP Option)

Feed Motor (X/Z Axis)				AC 6 HP

Live Tool Motor (VL-100CM only)				AC 20HP

COOLING SYSTEM

Pump 1 – Bed Washing				3 Bar

Pump 2 – Coolant Thru Spindle				3 Bar C Type

10 Bar M Type

GENERAL

Net Weight (VL-100C / VL-100CM)				34,100 lbs. / 36,000 lbs.

Floor Space (LxW)				159.45” x 114.17”

Maximum Height				157.74”

Power Requirement (VL-100C / VL-100CM)				75 KVA / 90 KVA

Coolant Tank Capacity				400 liters

FANUC Oi-T CONTROL FEATURES

- 400 Registerable Programs

- 8.4” Color High Resolution LCD

- Absolute/Incremental Command

- Additional Macro Common Variables 100-199

- Auto Acceleration/Deceleration

- Auxiliary Function Lock

- Background Editing

- Backlash Compensation

- Canned Cycles for Drilling

- Canned Cycles G90-G92-G94

- Constant Surface Speed Control

- Controlled Axis:  2

- Custom Macro B

- Data Protect Key

- Decimal Point Input

- Dry Run

- Dwell (G04)

- Fanuc Alpha I AC Digital Servo and Spindle Systems with 1,000,000 Pulse Encoders

- Feedrate Override 50~150%

- Full MDI Keyboard

- Graphics Function (3D)

- Inch/Metric Conversion

- Incremental Feed (X1, X10, X100, X1000)

- Machine Lock (All Axis)

- Manual Feedrate Override (0-150%)

- Multiple Repetitive Canned Cycles (G70-G76)

- Optional Block Skip

- Polar Coordinates

- Program Input/Output or DNC Operation from PCMCIA Card on Front Panel (Up to 2GB Storage)

- Program Memory 640 Meters (265K)

- Program Stop/Program End (M00, M01, M02, M03)

- Programmable Input (G10)

- Rapid Traverse Override (0-100%)

- Reference Point Return (G27, G28)

- RS232 (reader/puncher interface)

- Run Hour and Parts Count Display

- Second Reference Point Return

- Single Block

- Skip Signal and High Speed Skip Signal

- Spindle Orientation M-19 (1 position)

- Spindle Speed Override (50~120%)

- Stored Pitch Error Compensation

- Stored Stroke Check 1

- Tool Geometry/Wear Offsets 64 Pairs

- Tool Length Compensation (G43, G44, G49)

- Tool Nose Radius Compensation (G40-G42)

- X Axis Radius/Diameter Programming

MACHINE PRICES

Honor VL-100C with Fanuc 0i-T Control, list	$POR

Honor VL-100CM with Fanuc 0i-T Control, list	$POR

TOOLING OPTIONS

Tooling for VL-100C

Tool holder Base GC-200  (6 are included with machine) 	$1,550

OD/Face tool holder IDF-1.25-200-200  (2 are included with machine) 	$1,500

Boring Tool Holder IFL-1.0-120-250  (2 are included with machine) 	$1,500

Drilling Boring Holder BOS-2.5-140-200  (2 are included with machine) (2.5” – 3.0” Opt.)	 $1,250

Tooling For VL-100CM

Tool holder base BT-50-200  (6 are included with machine)	$2,100

OD/Face tool holder IDF-1.25-200-200  (2 are included with machine)	 $1,500

Boring Tool Holder IFL-1.0-120-250  (2 are included with machine) 	$1,500

Boring Tool holder BOS-2.5-140-200  (2 are included with machine) (2.5” – 3.0” Opt.)	 $1,250

BT-50 Pull studs, each	$25.00

Other Tool Holder & Special Tool Holder	POR

MACHINE OPTIONS

Hydraulic Chuck & Cylinder, size selections	POR

Hard Jaws of Hydraulic Chuck	POR

High & Low Pressure Chucking	POR

Programmable Rail (3) Steps of 7.87 inches….……………………………………………….…….…$43,000

Power Chuck Adapter (factory installation)	$12,200

60HP Spindle Motor up grade	$21,500

Air Conditioner for Electrical Cabinet	$3,500

Power Transformer, external	$7,900

Oil Skimmer (disk type)	$2,700

Tool Pre-setter Inside (turning dia. is smaller than spec.)	$15,000

Linear Scale X Axis	$10,500

Linear Scale Z Axis	$6,500

ZF Gear Box for Live Tool Spindle	$19,500

Chip Conveyor, scraper type	$5,000

Manual Guide		$4,900

Lubrication Chiller for Main Spindle Bearing and Gear	$6,500.00

# Text boxes

*All accuracies stated are (JIS Standard) and are guaranteed only if the machine is installed in a temperature controlled environment along with the proper foundation meeting the minimum requirements of the machine tool builder. Please Contact CNC Systems for the specific machine requirements.